| FIAT 500 / 500C* Technical Specification |
| --- |
|  | 1.2 69hp | 1.2 69hp Dualogic | TwinAir 85hp | TwinAir 85hp Dualogic | TwinAir 105hp | MultiJet II 95hp |
| Engine Capacity | 1,242cc | 1,242cc | 875cc | 875cc | 875cc | 1,248cc |
| Engine Family | FIRE inline 4 | FIRE inline 4 | TwinAir 2-cyl | TwinAir 2-cyl | TwinAir 2-cyl | MultiJet II |
| Bore/Stroke(mm) | 70.8x78.9 | 70.8x78.9 | 80.5x86 | 80.5x86 | 80.5x86 | 69.6x82.0 |
| Comp Ratio | 11.1:1 | 11.1:1 | 10.0:1 | 10.0:1 | 10.0:1 | 16.8:1 |
| Aspiration | Atmospheric | Atmospheric | Turbo | Turbo | Turbo | Turbo |
| Injection System | Multipoint Electronic | Multipoint w detonation ctrl & valve actuation | MultiJet II |
| Cam Drive | Toothed Belt | Toothed Belt | Chain | Chain | Chain | Chain |
| Cam Type | SOHC | SOHC | Fully Variable | Fully Variable | Fully Variable | DOHC |
| Valves / Cylinder | 2 | 2 | 4 | 4 | 4 | 4 |
| Gearbox | Manual 5-sp | Dualogic 5-sp | Manual 5-sp | Dualogic 5-sp | Manual 6-sp | Manual 5-sp |
| Clutch | Mechanical | Mechanical | Hydraulic | Hydraulic | Hydraulic | Hydraulic |
| Max hp@rpm | 69 @ 5,500 | 69 @ 5,500 | 85 @ 5,500 | 85 @ 5,500 | 105 @ 5,500 | 95 @ 4,000 |
| Max Nm@rpm | 102 @ 3,000 | 102 @ 3,000 | 145 @ 1,900 | 145 @ 1,900 | 145 @ 2,000 | 200 @ 1,500 |
| 0-100km/h | 12.9 s | 12.9 s | 11.0 s | 11.0 s | 10.0 s | 10.7 |
| Top Speed | 159km/h | 159km/h | 172km/h | 172km/h | 188km/h | 180km/h |
| Dimensions(mm) | L 3571 / W 1627 (1893 incl. mirrors) / H 1488 / WB 2300 |
| Track F/R(mm) | 1413 / 1407 |
| F Brake Discs(mm) | 257 solid disc | 257 ventilated | 257 solid disc |
| R Brakes mm | 180 drum | 240 solid disc | 180 drum |
| Standard Tyres | 175/65 R14 | 175/65 R14 | 185/55 R15 | 185/55 R15 | 185/55 R15 | 185/55 R15 |
| Fuel Tank Volume | 35 litres |
| Boot Size (VDA) | 185 dm3 |
| Steering | Rack & Pinion Dual-Mode Electric PAS – Turning Circle 9.3m (kerb to kerb) |
| Suspension | Front MacPherson strut with anti-roll bar / Rear torsion beam with anti-roll bar |
| Kerb Weight(Kg) | 865/905* | 900/940* | 930/970* | 930/970* | 940/980* | 980/1020* |
| Towing Weight | 800kg (braked) / 400kg (non-braked) |
| Comb. L/100km | 4.7 | 4.5 | 3.8 | 3.8 | 4.2 | 3.4 |
| Ex. Urb L/100km | 4.3 | 4.0 | 3.4 | 3.5 | 3.5 | TBC |
| Urban L/100km | 5.5 | 5.4 | 4.6 | 4.3 | 5.5 | TBC |
| CO2 Emissions | 110g/km | 105g/km | 90g/km | 88g/km | 99g/km | 89g/km |

*Cabriolet